## Slide 1: MATLAB image anaysis
Josh Yeh

## Slide 2: results from google survey topics of interest…
MATLAB basics
workflow
GUI
plotting
write my own scripts
manip. prewritten scripts for sp
manip. prewritten scripts for DA

## Slide 3
Computer and MATLAB basics (what you need to know)
image analysis can be resource intensive
512 px
512 px
uncompressed RGB 8-bit image 6 Mb
30 fps 180 Mb/s
60s video 11 Gb
ideal computer specifications for image analysis
i7 quad-core with at least 6MB cache size (the brain of the computer)
16 GB RAM (Random Access Memory) (items on your desk)
>1 TB storage (Random Access Memory) (items in the file cabinet)
dedicated Nvidia graphics card (useful for visualizing 3D or 4D plots)
256 GB SSD storage to run Windows 10 and MATLAB

## Slide 4: image basics
0
col
row
x
y
color depth
8-bit: 0-255
12-bit: 0-4095
16 bit: 0-65535

## Slide 5: image formats
currently raw, uncompressed tiff images and raw, uncompressed avi 2.0 are implemented in the scripts
1) loss-less (more efficient way of storing data)
2) lossy (loss of information)
2 types of compression:
How images are compressed are often proprietary…
no information is lost for uncompressed images, but image size will be large

## Slide 6: Work flow
image collection
pre-processing
(corrections, etc.)
analysis
results
MATLAB scripts
depend on similar functions
create your own!
GitHub
maintain version control

## Slide 7: GitHub
MATLAB functions
download
functions and sync
Master copy
propose changes
changes are approved and implemented
erc-chemech/Nikon_stitch_GUI

## Slide 8: Setting up MATLAB with Github library
Create/sign-in to your Github account
Download Github desktop program
Subscribe and download repository (library):
  https://github.com/erc-chemech/image-processing-MATLAB
Create a startup.m file in your “C:/Documents/MATLAB” folder
Add the library path to startup.m
  e.g. addpath(‘C:/Documents/GitHub/image-processing-MATLAB’);
Make sure to download all available toolboxes

## Slide 9: startup.m example
%Script that runs at startup
clc;
disp(date);
addpath('F:\Dropbox\ESPCI-Paris\MATLAB\image-processing-MATLAB');
disp('Startup script for Josh initiated!');

## Slide 10: Overview of image-processing-MATLAB library
image analysis
fitting
plotting
misc.
Argolight.m
bin_data_array.m
coord2image.m
extract_frames.m
gen_sf_array.m
import_tiff_stack.m
play_frames.m
px_coord2image.m
rgb_correction.m
rgb_ratio.m
DA_image_analysis/corrections.m
DA_image_analysis/DA_ROI.m
DA_image_analysis/ex_subl.m
DA_image_analysis/mask_denoise.m
sp_crack_map_L/parse_sp_crack02b.m
sp_crack_map_LU/parse_sp_crack02.m
sp_crack_map_LU/gen_unload_array.m
dist_dsearch.m
fminsearchbnd.m
numerFminS.m
sp_crack_map_LU/TLS_refine.m
sp_crack_map_LU/mypoly2.m
center_axes.m
gen_labels.m
histfit_mod.m
my_color_gradient.m
my_fig.m
shadedErrorBar.m
subtightplot.m
xylabels.m
xyzlabels.m
sp_crack_map_L/alphaColorbar.m
sp_crack_map_L/alphaColorbar_stacked.m
sp_crack_map_L/honeycomb.m
sp_crack_map_L/my_hist2.m
sp_crack_map_L/my_honeycomb.m
sp_crack_map_LU/alphaColorbar.m
sp_crack_map_LU/alphaColorbar_stacked.m
sp_crack_map_LU/honeycomb.m
sp_crack_map_LU/my_hist2.m
sp_crack_map_LU/my_honeycomb.m
sp_crack_map_LU/ G_RGB_mod_space.m
sp_crack_map_LU/overlay_axes.m
findobj.m
sp_crack_map_L/my_dcm
sp_crack_map_L/getErr.m
sp_crack_map_LU/my_dcm
sp_crack_map_LU/getErr.m
sp_crack_map_LU/my_dcm_callback.m
functions are well commented

## Slide 11
Performing image analysis for DA, bond breakage experiments
Performing image analysis for spiropyran color analysis
image correction
noise removal
image stitching
step cyclic loading test
color mapping
crack tip mapping

## Slide 12: Image analysis (DA experiments)
image correction
flatfield correction
Obtain homogeneous samples containing activated DA mechanophore in PEA.
flatfield.m
calibration files
flatfield correction array
(divide image by this array to get corrected image)
flatfield.m demonstration

## Slide 13: Image analysis (DA experiments)
image correction (Argolight)
x-y distortion
Argolight calibration fluorescent dots
(with known spacing)
Argolight.m

## Slide 14: Image analysis (DA experiments)
image correction (Argolight)
x-y distortion
Argolight.m
input calibration image
x-y distortion
identify grid points
rotation correction
determine distortion

## Slide 15: Image analysis (DA experiments)
image correction (Argolight)
flatfield correction
generally not recommended
due to stage/sample tilting issues and Moiré effects
Argolight demonstration

## Slide 16: Image analysis (DA experiments)
image correction
general approach
Extract image (import_tiff_stack)
2) Perform flatfield correction (flatfield.m)
3) Perform distortion correction (Argolight.m)
convert image to xy coordinates
4) Perform 2d histogram binning
convert xy coordinates to image

## Slide 17: Image analysis (DA experiments)
noise removal
Use medfilt2 on image array (takes median value within an m by n array around the pixel.
lose image resolution
Use mask_denoise instead
1) medfilt2 on image array
2) binarize the image
3) perform further denoising operations on binary mask
4) apply mask to original image
remove noise
maintain original resolution
identify sample edge
denoising demonstration

## Slide 18: Image analysis (DA experiments)
image stitching

## Slide 19: Image analysis (DA experiments)
image stitching GUI
https://github.com/erc-chemech/image-processing-MATLAB

## Slide 20
Performing image analysis for DA, bond breakage experiments
Performing image analysis for spiropyran color analysis
image correction
noise removal
image stitching
step cyclic loading test
color mapping
crack tip mapping

## Slide 21: Image analysis (sp experiments)
Define region as a “white reference”
Unimportant whether the white reference is “truly” white, since only relative color change is important.
step cyclic loading test
Perform color correction
  Rescale and re-center RGB values
  Needed in order to compare color changes between different samples

## Slide 22: Image analysis (sp experiments)
Perform color correction
  Rescale and re-center RGB values
  Needed in order to compare color changes between different samples
step cyclic loading test

## Slide 23: Image analysis (sp experiments)
Why not re-center channels at a value of 255?
  This is to prevent saturated pixels when displaying the corrected image.
  It does not matter what value you center at, since the values are normalized by the sum of the 3 channels (RGB ratio)
Quantify color change with RGB ratio
R or G or B
R+G+B
Derivable from Grassman’s Law from colorimetry
step cyclic loading test

## Slide 24: Image analysis (sp experiments)
Identify region-of-interest (ROI)
  Based on black markings on sample
Perform calculations (mean, stdev, etc.)
step cyclic loading test
soon to be incorporated into library…
step cyclic loading demonstration

## Slide 25: Image analysis (sp experiments)
color mapping
associate color with applied stress (complicated…)
soon to be incorporated into library…

## Slide 26
8x speed
no color
virgin loading
unloading
reloading
virgin loading
~1.7 MPa
Notes: So, let’s go back to the step cyclic experiment that I showed you from before. This time I will show you a synchronized color analysis. Since we only need 2 descriptors, we can describe the color changes with the total color change and the change in the green chromaticity. The choice for these 2 descriptors are semi-arbitrary, but the choice is based on the idea that the total color change represents the total “signal” given by the activation of the mechanophore and the observation that the green chromatic change is particularly sensitive to the unloading process of the sample.

## Slide 27
virgin loading
unloading
reloading
Stress (MPa)
total chromatic change
Notes: Simplified, labeled color map
Introduce isostress lines to create color-stress maps. (calibration map)
Based on the correlation, to back-calculate the associated stress for a given color.
Parse pixels as unloading vs. loading and determine the loading history for an unloaded pixel

## Slide 28: Image analysis (sp experiments)
color mapping
Instron data
synchronized and interpolated with video data
MATLAB “spline” fcn

## Slide 29: Image analysis (sp experiments)
color mapping
fit unloading/loading curves to chromatic points
3rd order polynomial
total least squares method
takes into account uncertainty in both x and y
numerFminS fcn
fit the fit parameters to interpolate

## Slide 30: Image analysis (sp experiments)
color mapping
fit unloading curves to stresses
linear least squares method

## Slide 31: Image analysis (sp experiments)
color mapping

## Slide 32: Image analysis (sp experiments)
crack tip mapping
parse_sp_crack02 fcn (also very complicated)
color
stress values
loading vs. unloading

## Slide 33: Image analysis (sp experiments)
crack tip mapping
loading vs. unloading
loading stresses are determined by closest orthogonal distance along the loading line

## Slide 34: Image analysis (sp experiments)
crack tip mapping

## Slide 35
Performing image analysis for DA, bond breakage experiments
Performing image analysis for spiropyran color analysis
image correction
noise removal
image stitching
step cyclic loading test
color mapping
crack tip mapping